## Slide 1
e7d195523061f1c0220a3acd2f99070e22f7f2176c6c61f4AB5BC6AF3DF28E09514168BD2F6654DA4347BEC42B9A9B38EB2139F52FD80B94EB8F1B847F5BC18ECD11DB8433CCABD6DAEA8D49E99C31D30DD985C7E7F658688B7009348515AAB54ABFBB4983FE2756082B17EC8C2A625C2986296D34D71E7781AFBE705FC011F12C413BF69C59FBC185B890F34DF9788C
Optimal power disaggregation
among heterogeneous resources
for providing frequency regulation
Ruike Lyu (吕睿可)
Dec. 8, 2023
Lyu, Ruike, Hongye Guo, Kedi Zheng, Mingyang Sun, and Qixin Chen. "Co-optimizing Bidding and Power Allocation of an EV Aggregator Providing Real-time Frequency Regulation Service." IEEE Transactions on Smart Grid (2023).

## Slide 2
e7d195523061f1c0220a3acd2f99070e22f7f2176c6c61f4AB5BC6AF3DF28E09514168BD2F6654DA4347BEC42B9A9B38EB2139F52FD80B94EB8F1B847F5BC18ECD11DB8433CCABD6DAEA8D49E99C31D30DD985C7E7F658688B7009348515AAB54ABFBB4983FE2756082B17EC8C2A625C2986296D34D71E7781AFBE705FC011F12C413BF69C59FBC185B890F34DF9788C
Contents
Power Allocation Model Based on Lagrange Multipliers
04
Background and Motivation
01
The proposed framework
02
Optimal Bidding Model with Embedded Power Allocation
03
Case Study
05

## Slide 3
Background
August 2022: Power restriction in Sichuan. Chengdu residents using ice blocks to cool down after power restriction/Dimmed subway lights.
The novel power system needs more flexible resources！

## Slide 4
In 2021, the number of electric vehicles in Beijing exceeded 500,000, able to support one-fourth of the maximum load of Beijing.
From 2014 to 2021, the average cost of power batteries has dropped by more than 75%.
Background
V2G is becoming a reality!

## Slide 5
5
Due to the limited capacity of a single EV, EV aggregators (EVAs) usually need to aggregate a large number of EVs to meet the threshold for entering electricity market.
EVA-led charging management mode: three links
the EVA bidding in the market: deciding the regulation capacity
Background

## Slide 6
6
Due to the limited capacity of a single EV, EV aggregators (EVAs) usually need to aggregate a large number of EVs to meet the threshold for entering electricity market.
EVA-led charging management mode: three links
the EVA bidding in the market: deciding the regulation capacity
the EVA allocating (dis)charging power to EVs
Background

## Slide 7
7
Due to the limited capacity of a single EV, EV aggregators (EVAs) usually need to aggregate a large number of EVs to meet the threshold for entering electricity market.
EVA-led charging management mode: three links
the EVA bidding in the market: deciding the regulation capacity
the EVA allocating (dis)charging power to EVs
the revenue distribution between the EVA and EV owners
Background
The three links are coupled but often regarded as decoupled and optimized separately for complexity issues. A practical framework for co-optimizing EVA bidding and power allocation is challenging!

## Slide 8
8
Why co-optimizing?
a. In the EVA bidding problem, it is necessary to consider the power allocation strategy in regulation deployment because different allocation strategies will induce different costs, especially when the EVs feature heterogeneous degradation costs, charging efficiencies, and other characteristics.
Motivation
Intuition: allocate discharging power to the EVs with lower degradation costs!
What if always allocating discharging power to the EVs with lower degradation costs?
Reduce 15 kW!
- 15 kW?

## Slide 9
9
Why co-optimizing?
b. As a result of the market operation process, bidding and power allocation are alternating and process coupled. The bids for a certain time interval determine the regulation power to be allocated in the interval, and the power allocation results determine the feasible bidding range for the next time intervals by affecting the SOCs of the EVs.
Motivation

## Slide 10
10
Why challenging?
Calculation time: Following the regulation signals that are issued every few seconds means that the (dis)charging power of thousands of EVs needs to be determined online.
Uncertainty: Regulation (AGC) signals are not known in advance.
Motivation
RegD signal form PJM, 18.07.2022
How to online solve stochastic optimization with a large number of scenarios?

## Slide 11
11
Literature Review
There is no research that reasonably models the coupling and provides a practical framework that meets the time constraints required for regulation deployment.
This problem exists in aggregating EVs, energy storages, HVAC and other resources.
Proportionally allocation.
Heuristic weights.

## Slide 12
12
Contribution
We propose a framework to co-optimize the bidding and power allocation of an EVA in the regulation market. The bidding model is formulated as stochastic optimization with embedded power allocation in discretized regulation signal scenarios.
To meet the computation time requirement for regulation deployment, we propose a power allocation model using the Lagrange multipliers from the bidding model, which can be calculated online. This determines the allocated power that corresponds to the optimal solution of the bidding model.
The case study verifies the effect of considering the coupling between bidding and power allocation on improving the EVA profit and reducing EV battery degradation costs.

## Slide 13
e7d195523061f1c0220a3acd2f99070e22f7f2176c6c61f4AB5BC6AF3DF28E09514168BD2F6654DA4347BEC42B9A9B38EB2139F52FD80B94EB8F1B847F5BC18ECD11DB8433CCABD6DAEA8D49E99C31D30DD985C7E7F658688B7009348515AAB54ABFBB4983FE2756082B17EC8C2A625C2986296D34D71E7781AFBE705FC011F12C413BF69C59FBC185B890F34DF9788C
Contents
Power Allocation Model Based on Lagrange Multipliers
04
Background and Motivation
01
The proposed framework
02
Optimal Bidding Model with Embedded Power Allocation
03
Case Study
05

## Slide 14
14
The proposed framework
Real-time frequency regulation market.
EVA Contracts with EV owners.
Bidding module (B)
Power allocation module (A2)

## Slide 15
15
The proposed framework
Real-time frequency regulation market.
EVA Contracts with EV owners.
Bidding module (B)
Power allocation module (A2)

## Slide 16
16
The proposed framework
Bidding module (B)
Data preparation: the EVA collects the arriving and leaving time, current SOCs, charging needs, and battery parameters of the EVs and generates forecasts about prices and regulation signals according to historical market data.
Optimal bidding: based on these parameters, the bidding module outputs the latest optimal bids, and the Lagrange multipliers can be obtained without additional computational overhead.
Power allocation submodule (A1) embedded in the bidding module (B): the power allocation in each regulation signal scenarios is simultaneously optimized.
actual regulation signals

## Slide 17
17
The proposed framework
Optimal power allocation module (A2)
We design a power allocation module (A2) to quickly decide the (dis)charging power of the EVs in regulation deployment.
Why A2?
The power allocation results (A1) in the bidding model only correspond to the discretized regulation signal scenarios (e.g., [0, 0.1), ..., [0.9, 1),...), while the actual regulation signal may take any value in its nearly continuous range (e.g., 0.9998). Therefore, the bidding model cannot be directly used to respond to regulation signals.
actual regulation signals

## Slide 18
e7d195523061f1c0220a3acd2f99070e22f7f2176c6c61f4AB5BC6AF3DF28E09514168BD2F6654DA4347BEC42B9A9B38EB2139F52FD80B94EB8F1B847F5BC18ECD11DB8433CCABD6DAEA8D49E99C31D30DD985C7E7F658688B7009348515AAB54ABFBB4983FE2756082B17EC8C2A625C2986296D34D71E7781AFBE705FC011F12C413BF69C59FBC185B890F34DF9788C
Contents
Power Allocation Model Based on Lagrange Multipliers
04
Background and Motivation
01
The proposed framework
02
Optimal Bidding Model with Embedded Power Allocation
03
Case Study
05

## Slide 19
19
We use the degradation model for EV batteries* where the battery degradation is based on the depth of discharge (DOD) and can be linearly approximated by discharge segments.
Bidding Model
* S. Han, S. Han, and H. Aki, “A practical battery wear model for electric vehicle charging applications,” Applied Energy, vol. 113, pp. 1100–1108, Jan. 2014.

## Slide 20
20
Net power of the EVs follows the regulation signal in each regulation signal scenario.
Bidding Model
The expected change of EV i in SOC across the time intervals.
The entire model, formulated as a stochastic linear programming problem, can be efficiently solved by commercial solvers.

## Slide 21
e7d195523061f1c0220a3acd2f99070e22f7f2176c6c61f4AB5BC6AF3DF28E09514168BD2F6654DA4347BEC42B9A9B38EB2139F52FD80B94EB8F1B847F5BC18ECD11DB8433CCABD6DAEA8D49E99C31D30DD985C7E7F658688B7009348515AAB54ABFBB4983FE2756082B17EC8C2A625C2986296D34D71E7781AFBE705FC011F12C413BF69C59FBC185B890F34DF9788C
Contents
Power Allocation Model Based on Lagrange Multipliers
04
Background and Motivation
01
The proposed framework
02
Optimal Bidding Model with Embedded Power Allocation
03
Case Study
05

## Slide 22
22
The second term in the objective function is a penalty term, which forces the EVA to follow the regulation signal as closely as possible.
The cost is calculated from the battery degradation cost that is immediately generated by EV discharge in addition to the impact on future EVA profit accounted for through the Lagrange multiplier, which will be analyzed later.
Power Allocation Model
…

## Slide 23
23
Power Allocation Model
In this paper, the optimality of the power allocation problem refers to the fact that its output (allocated power) corresponds to the optimal power allocation given by the bidding problem.
Power allocation problem
Bidding problem
Intuitively, the Lagrange multiplier of the SOC constraint represents the shadow price of SOC for the profit of EVA bidding, i.e., the cost of increasing a unit SOC of EV i at t.
By considering the impact on future EVA profit through together with the immediately induced degradation cost, the solution to the power allocation problem maximizes EVA profit.

## Slide 24
24
Power Allocation Model
In the mathematical meaning, introducing Lagrange multipliers of the bidding problem into the power allocation problem makes the optimality conditions of the two problems correspond. Our analysis is based on the following assumptions:

## Slide 25
For Extension
 | Power limit
 | Energy limit
 | Change of energy
 | Initial energy
 | Response cost
We extended the optimal operation framework to VPPs composed of various distributed resources: establish a standardized model that can express the operating characteristics of multiple distributed resources and everything can be easily applied!

## Slide 26
e7d195523061f1c0220a3acd2f99070e22f7f2176c6c61f4AB5BC6AF3DF28E09514168BD2F6654DA4347BEC42B9A9B38EB2139F52FD80B94EB8F1B847F5BC18ECD11DB8433CCABD6DAEA8D49E99C31D30DD985C7E7F658688B7009348515AAB54ABFBB4983FE2756082B17EC8C2A625C2986296D34D71E7781AFBE705FC011F12C413BF69C59FBC185B890F34DF9788C
Contents
Power Allocation Model Based on Lagrange Multipliers
04
Background and Motivation
01
The proposed framework
02
Optimal Bidding Model with Embedded Power Allocation
03
Case Study
05

## Slide 27
27
We used historical market data in July 2022 from PJM. We assumed that the prices can be accurately forecasted while the regulation-signal-related parameters in the bidding problem are forecasted results.
Case Study
联络线交换功率、容量价格均收敛

## Slide 28
28
Case Study
联络线交换功率、容量价格均收敛

## Slide 29
29
Case Study
联络线交换功率、容量价格均收敛
EV211: Type a (low degradation cost), arrived at 18:00 on the 17th and left at 10:00 on the 18th).
Proportional Allocation: failing to utilize the low degradation cost of EV211.
Minimum Degradation: ignoring the impact of discharging EV211 on future EVA profit.
Heuristic Weight: partially reconciles the aim of reducing degradation costs and increasing future income.
Proposed Method: optimal.

## Slide 30
30
Case Study
联络线交换功率、容量价格均收敛
Compared to the Proportional Allocation method (blue), the increase ratio of profits using the proposed method (red) ranges between 6.5% and 41.3%, and the total profit of the 14 days is increased by 13.4%.
Compared with the Proportional Allocation method (blue), when the degradation factors are 1, 2, and 4 times the default value, the EVA profits using the proposed method (red) are 16.7%, 42.4%, and 61.0% higher, respectively.

## Slide 31
31
Case Study
联络线交换功率、容量价格均收敛
Although our assumptions are not all true, the proposed framework works well!

## Slide 32
32
Conclusion
联络线交换功率、容量价格均收敛
An EVA's bidding in the regulation market is coupled with its power allocation strategy for regulation deployment. Considering this coupling improves the EVA profit.
The simulation results verify that co-optimizing bidding and power allocation enables both utilizing the heterogeneous characteristics of the EVs and balancing the short/long-term costs, thus improving the profit of the EVA while reducing the degradation costs.
The profit distribution between the EVA and EVs is also coupled with bidding and power allocation. In addition, the forecast of regulation signals could be improved. These issues are for future research.

## Slide 33
e7d195523061f1c0220a3acd2f99070e22f7f2176c6c61f4AB5BC6AF3DF28E09514168BD2F6654DA4347BEC42B9A9B38EB2139F52FD80B94EB8F1B847F5BC18ECD11DB8433CCABD6DAEA8D49E99C31D30DD985C7E7F658688B7009348515AAB54ABFBB4983FE2756082B17EC8C2A625C2986296D34D71E7781AFBE705FC011F12C413BF69C59FBC185B890F34DF9788C
Thanks for Listening!
Q & A
Ruike Lyu (吕睿可)
Lyu, Ruike, Hongye Guo, Kedi Zheng, Mingyang Sun, and Qixin Chen. "Co-optimizing Bidding and Power Allocation of an EV Aggregator Providing Real-time Frequency Regulation Service." IEEE Transactions on Smart Grid (2023).